## Slide 1: GPIO Learning Sharing
Zhang Liu
zhang.liu@intel.com
2014-08-19

## Slide 2: Table of Contents
linux kernel module
linux driver
gpio code
a character linux driver to blink LED
Reference

## Slide 3: linux kernel module
  linux module scheme is for dynamicly controlling linux kernel.
  module is not compiled into kernel,so the size of kernel can be controlled
  once be loaded,module can be seen part of kernel
  module can be added or deleted as ordinary softwares.
    static int __init myModule_init(void)
    static void __exit myModule_exit(void)
    module_init(myModule_init)
    module_exit(myModule_exit)
    MODULE_AUTHOR("");
    MODULE_LOCENSE("");
  module compile
  module load -insmod lsmod rmmod dmesg
    through kernel symbol table
    EXPORT_SYMBOL(referenced_function) to provide a function to be referenced
    extern type referecned_function to use

## Slide 4: linux driver
    char drivers, Block Drivers , Network Drivers and others
      Block: block device
      Devices: all devices organized by bus type
      bus: all bus type
      Dirvers: all drivers registered
      class: all device organzied by class type
      firmware and power
      The kobject is the fundamental structure that holds the device model together
      Ksets are kobejct that with same type
      subsystems use to describes a kind of device subsystem

## Slide 5: gpio code
  gpio driver code mainly composites of gpiolib.c and gpio-sch.c
  gpiolib.c code provides sysfs for user interface and export function for other module reference
  gpio-sch.c code is the driver code that interacts with hardware and provide function interfaces to gpiolib.c.
    gpio code interact with hardware through registers:CGEN, CGIO, CGLV, CGTPE ,CGTNE, CGGPE, CGSMI, CGTS, RGEN, RGIO, RGLV, RGTPE, RGTNE,RGGPE, RGSMI ,RGTS,CGNMIEN,RGNMIEN
    CGTPE interrupt enable of core gpio when input from 0-1
    CGTNE interrupt enable of core gpio when input from 1-0
    CGTS :if CGTPE set, 0-1 trigger interuppt,if CGTNE set, 1-0 trigger interupt -
    …………………..

## Slide 6: gpio-sch.c
  the driver code of gpio-sch.c use linux driver framework of platform
  sch_gpio_probe, sch_gpio_remove, sch_gpio_suspend_sys, sch_gpio_resume_sys, are defiened in gpio-sch.c to fullfill the framework
static struct platform_driver sch_gpio_driver = { .driver = { .name = "sch_gpio", .owner = THIS_MODULE, }, .probe = sch_gpio_probe, .remove = sch_gpio_remove, .suspend = sch_gpio_suspend_sys, .resume = sch_gpio_resume_sys, }; module_platform_driver(sch_gpio_driver);

## Slide 7: interrupts
  gpio driver code implement functionality of input through interrupts
    irq_alloc_descs is clalled to allocate "irq_descs" for core and resume port of gpio
gpio-sch.c/689 chip->irq_base_core = irq_alloc_descs(-1, 0, sch_gpio_core.ngpio, NUMA_NO_NODE); gpio-sch.c/698 chip->irq_base_resume = irq_alloc_descs(-1, 0, sch_gpio_resume.ngpio, NUMA_NO_NODE);
  request_irq is called to request interrupt from kernel, irq_num is the interuppts number for apply, "sch_gpio_irq_handle" is interrupt function , IRQF_SHARED is the tag of sharing interrupt.
gpio-sch.c/718 err = request_irq(irq_num, sch_gpio_irq_handler, IRQF_SHARED, KBUILD_MODNAME, chip);

## Slide 9: interrupt intialization of every gpio port
  sch_gpio_core_irqs_init and sch_gpio_resume_irqs_init will set coresponding chip data using "irq_set_chip_data" , set irq_chip pointer variable and interrupt handler for each gpio port using "irq_set_chip_and_handler_name".
gpio-sch.c/726 static void sch_gpio_core_irqs_init(struct sch_gpio *chip, unsigned int num) { int i; for (i = 0; i < num; i++) { irq_set_chip_data(i + chip->irq_base_core, chip); irq_set_chip_and_handler_name(i + chip->irq_base_core, &sch_irq_core, handle_simple_irq, "sch_gpio_irq_core"); } } gpio-sch.c/727 sch_gpio_resume_irqs_init(chip, sch_gpio_resume.ngpio);

## Slide 11: interrupt handler
static irqreturn_t sch_gpio_irq_handler(int irq, void *dev_id) { int res; int i, ret = IRQ_NONE; for (i = 0; i < sch_gpio_core.ngpio; i++) { res = sch_gpio_reg_get(CGTS, i); if (res) { /* clear by setting TS to 1 */ sch_gpio_reg_set(CGTS, i, 1); generic_handle_irq(chip_ptr->irq_base_core + i); ret = IRQ_HANDLED; } } for (i = 0; i < sch_gpio_resume.ngpio; i++) { res = sch_gpio_reg_get(RGTS, i); if (res) { /* clear by setting TS to 1 */ sch_gpio_reg_set(RGTS, i, 1); generic_handle_irq(chip_ptr->irq_base_resume + i); ret = IRQ_HANDLED; } } return ret; }
  function "sch_gpio_irq_handler" will check every gpio port to find the interrupt source, if detects a port,will call generic_handle_irq to deal with the interrupt.

## Slide 12: how sysfs interfaces is created?
    codes that use to init a gpio class in sysfs can be found in gpiolib_sysfs_init function
gpiolib.c/1097 static int __init gpiolib_sysfs_init(void) gpiolib.c/1103 status = class_register(&gpio_class); gpiolib.c/1122 status = gpiochip_export(chip); gpiolib.c/1130 postcore_initcall(gpiolib_sysfs_init);
  "class_register" function is called in "gpiolib_sysfs_init" to register gpio class under /sys/class/gpio
  "gpiochip_export" function is called in "gpiolib_sysfs_init" to create the class attributes of "export" and "unexport" which coresponds to two readonly files under /sys/class/gpio

## Slide 14: export a gpio port
  when write port number to file "export" under /sys/class/gpio, function export_store will be clalled and use gpio_export to creat coresponding directory and files under /sys/class/gpio
gpiolib.c/723 static ssize_t export_store(struct class *class, struct class_attribute *attr, const char *buf, size_t len) gpiolib.c/817 int gpio_export(unsigned gpio, bool direction_may_change)
  gpio_export create files under corespoding port directory, every file corepond to a attribute which has "show" and "store" functions that define "read" and "write" functions.
  the attributes are passed through gpio_attr_group, the attributes are declared below:
gpiolib.c/303 static /* const */ DEVICE_ATTR(direction, 0644, \ gpio_direction_show,gpio_direction_store); gpiolib.c/360 static const DEVICE_ATTR(value, 0644, gpio_value_show,\ gpio_value_store); gpiolib.c/540 static DEVICE_ATTR(edge, 0644, gpio_edge_show,\ gpio_edge_store); gpiolib.c/583 static const DEVICE_ATTR(active_low, 0644,\ gpio_active_low_show, gpio_active_low_store); gpiolib.c/658 static const DEVICE_ATTR(drive, 0644,\ gpio_drive_show, gpio_drive_store);

## Slide 15: how sysfs interact with gpio driver code
    gpio_chip struct contains functions that driver provides for fundemental gpio operations interfaces
gpio-sch.c/205 static struct gpio_chip sch_gpio_core = { .label = "sch_gpio_core", .owner = THIS_MODULE, .direction_input = sch_gpio_core_direction_in, .get = sch_gpio_core_get, .direction_output = sch_gpio_core_direction_out, .set = sch_gpio_core_set, .to_irq = sch_gpio_core_to_irq, };
    code in gpiolib.c/1161 define function that registers a gpio_chip to the gpio_desc, and the function is exported using EXPORT_SYMBOL
gpiolib.c/1161 int gpiochip_add(struct gpio_chip *chip);
  then gpiochip_add is used by gpio-sch.c to pass sch_gpio_core and sch_gpio_resume into gpio_desc
gpio-sch.c/681 err = gpiochip_add(&sch_gpio_core); gpio-sch.c/685 err = gpiochip_add(&sch_gpio_resume);

## Slide 17: call functions in gpio-sch.c through gpio_desc
static int gpio_get_direction(unsigned gpio) { struct gpio_chip *chip; struct gpio_desc *desc = &gpio_desc[gpio]; int status = -EINVAL; chip = gpio_to_chip(gpio); gpio -= chip->base; if (!chip->get_direction) return status; status = chip->get_direction(chip, gpio); if (status > 0) { /* GPIOF_DIR_IN, or other positive */ status = 1; clear_bit(FLAG_IS_OUT, &desc->flags); } if (status == 0) { /* GPIOF_DIR_OUT */ set_bit(FLAG_IS_OUT, &desc->flags); } return status; }
  gpiolib.c/201 "gpio_get_direction" for example, function get gpio_chip * varible chip which points to a "sch_gpio_core" or "sch_gpio_resume",and when "chip->getdirection" is called,correspending function in driver will be called.

## Slide 18: a character linux driver to blink LED

## Slide 19: character driver framework
a module init function
gpio_IO2IO3.c/129 int chardev_init(void);
a module exit function
gpio_IO2IO3.c/160 void chardev_exit(void);
operations in module init function
gpio_IO2IO3.c/132 ret = alloc_chrdev_region(&dev_num,0,1,DEVICENAME);
get major device number
gpio_IO2IO3.c/139 major_number = MAJOR(dev_num);
apply for memory for cdev
gpio_IO2IO3.c/143 mcdev = cdev_alloc();
register the cde
gpio_IO2IO3/148 ret = cdev_add(mcdev,dev_num,1);

## Slide 20: interact with the module
  to interact with the module using stand file read and write operations, drive code implement detail functionality through defining corespoding member function of file_operations struct.
gpio_IO2IO3.c/121 struct file_operations fops = { .owner = THIS_MODULE, .open = device_open, .write = device_write, .release = device_close, }; gpio_IO2IO3/144 mcdev->ops = &ops;

## Slide 21: file operations corespond to gpio
  open gpio 31/30 and output 1 into the ports to make port IO2(32) and IO3(18) work ,and make IO2 and IO3 output
gpio_IO2IO3/51 static int device_open(struct inode *inode, struct file *filp)
  if argument is "0",output IO2 1 and IO3 0,else if argument is "1",output IO2 0 and IO3 1
gpio_IO2IO3/91 static ssize_t device_write(struct file *fp, const char *buff, size_t length, loff_t *ppos)
  close function will free gpio port that opened in device_open and do some clean work
gpio_IO2IO3/108 static int device_close(struct inode *inode, struct file *filp)

## Slide 22: module compile and install
Makefile

## Slide 23: python test to blink the LED

## Slide 24: Reference
Linux Device Drivers, Third Edititon
A simple linux character driver
  linux设备驱动开发详解